|  |  | ALBERTA FOREST PRODUCTS ASSOCIATION 500, 10709 Jasper Avenue EDMONTON, ALBERTA T5J 3N3 PHONE: (780) 452-2841 FAX: (780) 455-0505 |
| --- | --- | --- |

A.F.P.A. Fall 2009 GRADE EXAM

Name:		____________________________________	Date:	______________________

Company:	____________________________________	Location: ____________________

Mark the answer you choose with an [X]. ONLY ONE ANSWER PER QUESTION PLEASE!

| 1. | Which of the following species is not in the SPF species group: |
| --- | --- |
|  | [ ] Balsam Fir | [ ] Lodgepole Pine | [ ] Jack Pine | [ ] Sitka Spruce |

| 2. | Lumber heated in a closed chamber, with or without moisture content reduction, until it reaches a core temperature of 56 degrees Celsius for a minimum of 30 minutes, is considered: |
| --- | --- |
|  | [ ] Heat Dried | [ ] Heat Sensor | [ ] Heat Treated | [ ] Heat Chamber |

| 3. | What piece of information, is required to be on a Grade Stamp: |
| --- | --- |
|  | [ ] Date of Production | [ ] Graders Name | [ ] Length of board | [ ] NLGA |

| 4. | Portion of a Branch or Limb cut through by a saw is called : |
| --- | --- |
|  | [ ] Vertical Grain | [ ] Knots | [ ] Flat Grain | [ ] DET |

| 5. | Which SLOPE of GRAIN has the LEAST NEGATIVE effect, on the STRENGTH of DIMENSION lumber: |
| --- | --- |
|  | [ ] 1 in 12 | [ ] 1 in 10 | [ ] 1 in 8 | [ ] 1 in 4 |
| 6. | Air Dried lumber UNDER 19% moisture content, should be grade stamped: |
|  | [ ] HT | [ ] S-GRN | [ ] S-GRN HT | [ ] S-Dry |

| 7. | In Structural Light Framing, Joist and Planks, SAW CUTS are restricted to what size? |
| --- | --- |
|  | [ ] Centerline Knot | [ ] Hole Size | [ ] Edge Knot | [ ] 1/2 of Edge Knot |

| 8. | Which grade CAN NOT be stamped on a 2x6 12 foot? |
| --- | --- |
|  | [ ] Construction | [ ] Sel. Str. | [ ] Stud | [ ] No. 2 |

| 9. | Which grade of 2x4 has the HIGHEST STERENGTH rating? |
| --- | --- |
|  | [ ] # 3 Structural | [ ] # 2 Structural | [ ] Standard | [ ] Construction |

| Mark the following DEFECTS under the correct CLASSIFICATION: |
| --- |
|  | Defect | Natural | Manufacturing | Seasoning |
| 10. | Splits | [ ] | [ ] | [ ] |
| 11. | Wane | [ ] | [ ] | [ ] |
| 12. | Shake | [ ] | [ ] | [ ] |

| Match the following MANUFACTURING DEFECTS to the correct DEPTH CLASSIFICATION: |
| --- |
|  | DEFECT | 1/64 inch | 1/32 inch | 1/16 inch | 1/8 inch | Over 1/8 inch |
| 13. | Heavy Skip | [ ] | [ ] | [ ] | [ ] | [ ] |
| 14. | Light Skip | [ ] | [ ] | [ ] | [ ] | [ ] |
| 15. | Medium Skip | [ ] | [ ] | [ ] | [ ] | [ ] |

| Mark the correct dressed WIDTH for the following: |
| --- |
| 16. | 2x3 S-GRN | [ ] 2 1/4" | [ ] 2 1/2" | [ ] 2 9/16" | [ ] 2 3/8" |
| 17. | 2x4 KD-HT | [ ] 3 1/2" | [ ] 3 3/8" | [ ] 3 9/16” | [ ] 4" |
| 18. | 2x6 S-DRY | [ ] 5 9/16" | [ ] 5 1/2" | [ ] 5 1/4 " | [ ] 5 7/16" |
| 19. | 2x8 S-GRN HT | [ ] 7 1/4" | [ ] 7 3/4" | [ ] 7 1/2" | [ ] 8" |
| Mark the correct dressed THICKNESS for the following: |
| 20. | 4x4 S-GRN HT | [ ] 3 3/4" | [ ] 3 1/2" | [ ] 4" | [ ] 3 9/16" |
| 21. | 2x12 S-GRN | [ ] 1 7/16" | [ ] 1 1/2" | [ ] 1 9/16" | [ ] 1 5/8" |
| 22 | 2x4 KD-HT | [ ] 1 1/2" | [ ] 1 9/16” | [ ] 1 3/8" | [ ] 1 5/8” |
| 23. | 4x4 KD-HT | [ ] 3 7/16" | [ ] 3 1/2" | [ ] 3 9/16" | [ ] 3 5/8" |

| Mark the Highest grade of Par.121 Stud that allows the following for a 2 x 6 - 92 5/8” long: |
| --- |
|  | DEFECT |  |  | STUD | ECONOMY |
| 24. | 1/8” inch Skip on WIDE FACE 4 feet long. | [ ] | [ ] |
| 25. | Decay COMPLETELY through NARROW FACE 5 1/2" inches long. | [ ] | [ ] |
| 26. | WANE 2/3 Thickness on END of NARROW FACE | [ ] | [ ] |
| 27. | 3/8" inch Crook | [ ] | [ ] |
| 28. | A Spike Knot, that occupies 25% of the CROSS SECTION | [ ] | [ ] |
| 29. | 3 inches of GOOD WOOD full length on WIDE face | [ ] | [ ] |

| Mark the HIGHEST grade of Par. 122 Light Framing that allows the following for a 2 x 4 16’ feet long: |
| --- |
|  | DEFECT | CONSTRUCTION | STANDARD | UTILITY | ECONOMY |
| 30. | A 2” inch Round Knot | [ ] | [ ] | [ ] | [ ] |
| 31. | Skip 1/4” inch deep 1 feet long | [ ] | [ ] | [ ] | [ ] |
| 32. | Slope of Grain 1 in 4 | [ ] | [ ] | [ ] | [ ] |
| 33. | Surface Shake 3 feet long | [ ] | [ ] | [ ] | [ ] |
| 34. | 3/4" inch GOOD WOOD on END of NARROW FACE 1 foot long | [ ] | [ ] | [ ] | [ ] |
| 35. | A 3 face Shake, with 1 3/4” inch deepest penetration | [ ] | [ ] | [ ] | [ ] |
| 36. | Wane 1/4 the Width full length | [ ] | [ ] | [ ] | [ ] |
| 37. | 100% Heart Stain | [ ] | [ ] | [ ] | [ ] |
| 38. | Split, 24 inches long | [ ] | [ ] | [ ] | [ ] |
| Mark the HIGHEST grade of Par. 124 Structural Light Framing and Joist & Planks that allows the following in a 2 x 10-12 feet long: |
|  | DEFECT | SEL STR | #1 | #2 | #3 | NONE |
| 39. | Wane completely across NARROW FACE on END | [ ] | [ ] | [ ] | [ ] | [ ] |
| 40. | Decay 2 inches wide by 2 inches long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 41. | A 3 inch EDGE KNOT | [ ] | [ ] | [ ] | [ ] | [ ] |
| 42. | Wane 2/3 Thickness 2 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 43. | Slope of Grain 1 in 6 | [ ] | [ ] | [ ] | [ ] | [ ] |
| 44. | Wane 2/3 Thickness FULL LENGTH | [ ] | [ ] | [ ] | [ ] | [ ] |
| 45. | Through Shake 3’ feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 46. | SURFACE Shake 1’ foot long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 47. | 1/16” inch Skip 6’ feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 48. | Skip 1/8 inch deep 6 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 49. | 25 % White Speck | [ ] | [ ] | [ ] | [ ] | [ ] |
| 50. | 1/2 Medium Warp | [ ] | [ ] | [ ] | [ ] | [ ] |
| 51. | 12 inch SPLIT | [ ] | [ ] | [ ] | [ ] | [ ] |
| 52. | (4 5/8) inches of GOOD-WOOD on WIDE FACE on END | [ ] | [ ] | [ ] | [ ] | [ ] |
| 53. | Wane 1/2 the WIDTH on END | [ ] | [ ] | [ ] | [ ] | [ ] |
| 54. | A 8” inch CENTERLINE KNOT | [ ] | [ ] | [ ] | [ ] | [ ] |
| 55. | Shake COMPLETELY through NARROW face (3 face) 1 foot long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 56. | 20% HEART STAIN | [ ] | [ ] | [ ] | [ ] | [ ] |

List the knot sizes for the following KD-HT 2 x 6’s

2 1/4"

57.	List the knot size:

3 3/4"

SIZE

58.	List the knot size:                                                                  2 3/4"

1”

2 1/4"                3/4"

# SIZE

59.	List the knot size

3/4"                                                                                                      3/4”

SIZE

2 1/4”                             2 1/4"

60.	List the knot size

1/2"

1/2”

SIZE

# Text boxes

3 3/4"

1-3/4”