|  |  | ALBERTA FOREST PRODUCTS ASSOCIATION 500, 10709 Jasper Avenue EDMONTON, ALBERTA T5J 3N3 PHONE: (780) 452-2841 FAX: (780) 455-0505 |
| --- | --- | --- |

A.F.P.A. FALL 2008 GRADE EXAM

Name:		____________________________________	Date:	______________________

Company:	____________________________________	Location: ____________________

Mark the answer you choose with an [X]. ONLY ONE ANSWER PER QUESTION PLEASE!

| 1. | Which of the following specie is in the SPF species group: |
| --- | --- |
|  | [ ] Doug Fir | [ ] Ponderosa Pine | [ ] Jack Pine | [ ] White Pine |

| 2. | The portion of a branch or limb cut through by the saw, results in what type of defect? |
| --- | --- |
|  | [ ] Shake | [ ] Knots | [ ] Warp | [ ] Checks |

| 3. | What piece of information, is NOT required to be on a Grade Stamp: |
| --- | --- |
|  | [ ] Mill ID Number | [ ] Species Group | [ ] Length of board | [ ] NLGA |

| 4. | Which is NOT part of the Trunk: |
| --- | --- |
|  | [ ] Leaves | [ ] Sapwood | [ ] Pith | [ ] Bark |

| 5. | In NLGA Par. 121 STUD, which defect has the most NEGATIVE effect on the STRENGTH of lumber: |
| --- | --- |
|  | [ ] White Speck | [ ] Wane | [ ] Wood Rays | [ ] Edge Knots |
| 6. | Kiln Dried lumber OVER 19% moisture content, must be grade stamped: |
|  | [ ] S-Dry | [ ] KD-HT | [ ] S-Grn or S-Grn HT | [ ] MC 15 |

| 7. | In Structural Light Framing, Joist and Planks, Spike Knots are restricted to what size? |
| --- | --- |
|  | [ ] Centerline Knot | [ ] Hole Size | [ ] Sawcut allowance | [ ] Edge Knot |

| 8. | Which grade stamp CAN be used on a 2x6 12 foot? |
| --- | --- |
|  | [ ] Construction | [ ] SEL.STR.. | [ ] Standard & BTR. | [ ] Utility |

| 9. | Which grade of 2x4 has the LOWEST STRENGTH rating? |
| --- | --- |
|  | [ ] # 3 Structural | [ ] # 2 Structural | [ ] Standard | [ ] Stud |

| Mark the following DEFECTS under the correct CLASSIFICATION: |
| --- |
|  | Defect | Natural | Manufacturing | Seasoning |
| 10. | Warp | [ ] | [ ] | [ ] |
| 11. | Knots | [ ] | [ ] | [ ] |
| 12. | Improper Trimming | [ ] | [ ] | [ ] |

| Match the following MANUFACTURING DEFECTS to the correct DEPTH CLASSIFICATION: |
| --- |
|  | DEFECT | Very Light | Light | Medium | Heavy | Very Heavy |
| 13. | 1/16” deep Skip | [ ] | [ ] | [ ] | [ ] | [ ] |
| 14. | 1/8” deep Skip | [ ] | [ ] | [ ] | [ ] | [ ] |
| 15. | 3 /16” deep Skip | [ ] | [ ] | [ ] | [ ] | [ ] |

| Mark the correct dressed WIDTH for the following: |
| --- |
| 16. | 2x10 S-GRN | [ ] 9 1/4" | [ ] 9 1/2" | [ ] 9 9/16" | [ ] 9 5/8" |
| 17. | 2x6 KD-HT | [ ] 5 1/2" | [ ] 5 9/16" | [ ] 5 5/8” | [ ] 6" |
| 18. | 2x3 S-DRY | [ ] 2 1/4" | [ ] 2 1/2" | [ ] 2 9/16 " | [ ] 2 7/8" |
| 19. | 2x4 S-GRN HT | [ ] 3 1/4" | [ ] 3 1/2" | [ ] 3 9/16" | [ ] 3 3/4" |
| Mark the correct dressed THICKNESS for the following: |
| 20. | 2x4 S-GRN HT | [ ] 1 3/4" | [ ] 1 1/2" | [ ] 2" | [ ] 1 9/16" |
| 21. | 2x12 S-DRY | [ ] 1 7/16" | [ ] 1 1/2" | [ ] 1 9/16" | [ ] 1 5/8" |
| 22 | 1x4 KD-HT | [ ] 1/2" | [ ] 9/16” | [ ] 3/4" | [ ] 7/8” |
| 23. | 4x4 KD-HT | [ ] 3 7/16" | [ ] 3 1/2" | [ ] 3 9/16" | [ ] 3 5/8" |

| Mark the Highest grade of Par.121 Stud that allows the following for a 2 x 4 - 92 5/8” long: |
| --- |
|  | DEFECT |  |  | STUD | ECONOMY |
| 24. | 1/8” inch Skip on NARROW FACE 1 foot long | [ ] | [ ] |
| 25. | Decay COMPLETELY through NARROW FACE 1 1/2" inches long. | [ ] | [ ] |
| 26. | 1” inch GOOD WOOD on NARROW FACE | [ ] | [ ] |
| 27. | 1/2" inch Crook | [ ] | [ ] |
| 28. | Shake COMPLETELY through NARROW FACE 12” inches long | [ ] | [ ] |
| 29. | A 1 3/4" inch EDGE KNOT | [ ] | [ ] |

| Mark the HIGHEST grade of Par. 122 Light Framing that allows the following for a 2 x 4 12’ feet long: |
| --- |
|  | DEFECT | CONSTRUCTION | STANDARD | UTILITY | ECONOMY |
| 30. | A 2 5/8” inch Round Knot | [ ] | [ ] | [ ] | [ ] |
| 31. | Skip 1/8” inch deep 3 feet long | [ ] | [ ] | [ ] | [ ] |
| 32. | Slope of Grain 1 in 6 | [ ] | [ ] | [ ] | [ ] |
| 33. | Through Shake | [ ] | [ ] | [ ] | [ ] |
| 34. | 1/2" inch GOOD WOOD on END of NARROW FACE | [ ] | [ ] | [ ] | [ ] |
| 35. | A 3 face Shake, with deepest penetration equaling 1” inch | [ ] | [ ] | [ ] | [ ] |
| 36. | Wane 3/4 the Width 2’ feet long | [ ] | [ ] | [ ] | [ ] |
| 37. | Decay 1/4 Cross Section | [ ] | [ ] | [ ] | [ ] |
| 38. | Split, 1 1/2 times width of piece in length | [ ] | [ ] | [ ] | [ ] |

| Mark the HIGHEST grade of Par. 124 Structural Light Framing and Joist & Planks that allows the following in a 2 x 6-16 feet long: |
| --- |
|  | DEFECT | SEL STR | #1 | #2 | #3 | NONE |
| 39. | Wane completely across WIDE FACE on END | [ ] | [ ] | [ ] | [ ] | [ ] |
| 40. | Decay 1/4" inch wide by 3” inches long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 41. | A 2 1/8” inch EDGE KNOT | [ ] | [ ] | [ ] | [ ] | [ ] |
| 42. | 1/2" inch of GOOD WOOD on NARROW FACE on END | [ ] | [ ] | [ ] | [ ] | [ ] |
| 43. | Slope of Grain 1 in 10 | [ ] | [ ] | [ ] | [ ] | [ ] |
| 44. | Wane 1/2 Thickness FULL LENGTH | [ ] | [ ] | [ ] | [ ] | [ ] |
| 45. | Through Shake 1’ foot long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 46. | SURFACE Shake 1’ foot long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 47. | 1/16” inch Skip 3’ feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 48. | Skip 1/8 inch deep 1 foot long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 49. | 1/2 the volume of White Speck | [ ] | [ ] | [ ] | [ ] | [ ] |
| 50. | Light Warp | [ ] | [ ] | [ ] | [ ] | [ ] |
| 51. | 9 inch SPLIT | [ ] | [ ] | [ ] | [ ] | [ ] |
| 52. | 2 1/4" inches of GOOD-WOOD on WIDE FACE on END | [ ] | [ ] | [ ] | [ ] | [ ] |
| 53. | Wane 1/2 the WIDTH 2 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 54. | A 2 3/4” inch CENTERLINE KNOT | [ ] | [ ] | [ ] | [ ] | [ ] |
| 55. | Wane Completely across Narrow Face 16” inches long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 56. | A 4” inch EDGE KNOT | [ ] | [ ] | [ ] | [ ] | [ ] |

List the knot sizes for the following KD-HT 2 x 4’s

1 1/4"

57.	List the knot size:

SIZE

1 5/8"

58.	List the knot size:

1/2"

1 1/4"                3/8"

# SIZE

59.	List the knot size

1/2"                                                                                                      3/4”

1 3/4”                                                             SIZE

60.	List the knot size

1/2"

1/2”

SIZE

# Text boxes

1 7/8"

1-3/4”