|  |  | ALBERTA FOREST PRODUCTS ASSOCIATION 500, 10709 Jasper Avenue EDMONTON, ALBERTA T5J 3N3 PHONE: (780) 452-2841 FAX: (780) 455-0505 |
| --- | --- | --- |

A.F.P.A. FALL 2010 GRADE EXAM

Name:		____________________________________	Date:	______________________

Company:	____________________________________	Location: ____________________

Mark the answer you choose with an [X]. ONLY ONE ANSWER PER QUESTION PLEASE!

| 1. | Which of the following species is a HARDWOOD ? |
| --- | --- |
|  | [ ] Tamarack | [ ] Aspen | [ ] Black Spruce | [ ] Lodgepole Pine |

| 2. | Which is NOT part of the trunk? |
| --- | --- |
|  | [ ] Bark | [ ] Pith | [ ] Leaves | [ ] Heartwood |

| 3. | Inner bark is also called? |
| --- | --- |
|  | [ ] Bast | [ ] Leader | [ ] Pits | [ ] Heartwood |

| 4. | Which is a desirable feature of lumber? |
| --- | --- |
|  | [ ] It Splits | [ ] It Burns | [ ] It Shrinks | [ ] It’s renewable |

| 5. | Water contained in the cell walls is called? |
| --- | --- |
|  | [ ] Bound Water | [ ] Free Water | [ ] Hard Water | [ ] Water Logged |

6-9.		Match the category name with the correct NLGA paragraph number. (e.g.     a    )

a)	Economy

6.	Para. 122			_________

b)	Light Framing

c)	MSR						7.	Para. 121			__________

d)	Structural Joist & Planks

8.	Para. 124			__________

e)	Stud

f)	#3						9.	Para. 122e			__________

| Mark the following DEFECTS under the correct CLASSIFICATION: |
| --- |
|  | Defect | Natural | Manufacturing | Seasoning |
| 10. | Wane | [ ] | [ ] | [ ] |
| 11. | Split | [ ] | [ ] | [ ] |
| 12. | Saw Cut | [ ] | [ ] | [ ] |

| Match the following MANUFACTURING DEFECTS to the correct CLASSIFICATION: |
| --- |
|  | DEFECT | Very light | Light | Medium | Heavy | Very Heavy |
| 13. | 1/8 inch Skip | [ ] | [ ] | [ ] | [ ] | [ ] |
| 14. | 1/2 inch Skip | [ ] | [ ] | [ ] | [ ] | [ ] |
| 15. | 1/4 inch Skip | [ ] | [ ] | [ ] | [ ] | [ ] |

| Mark the correct dressed WIDTH for the following: |
| --- |
| 16. | 2x4 KD-HT | [ ] 3 1/2" | [ ] 4" | [ ] 3 9/16" | [ ] 3 5/8" |
| 17. | 3x8 S-GRN | [ ] 7 1/2" | [ ] 8" | [ ] 7 1/4” | [ ] 7 9/16" |
| 18. | 2x10 KD-HT | [ ] 10 9/16" | [ ] 9” | [ ] 9 1/8 " | [ ] 9 1/4" |
| 19. | 4x4 S-GRN | [ ] 3 9/16" | [ ] 3 3/4" | [ ] 3 1/2" | [ ] 3 1/4" |

| Mark the correct dressed THICKNESS for the following: |
| --- |
| 20. | 2x4 KD-HT | [ ] 1 1/2" | [ ] 1 9/16" | [ ] 1 5/8" | [ ] 1 3/4" |
| 21. | 2x6 S-GRN | [ ] 1 7/16" | [ ] 1 1/2" | [ ] 1 9/16" | [ ] 1 5/8" |
| 22 | 4x4 S-DRY | [ ] 3 1/2 | [ ] 3 9/16 | [ ] 4 | [ ] 3 1/4 |
| 23. | 3x10 S-GRN | [ ] 2 7/16" | [ ] 2 1/2" | [ ] 2 9/16" | [ ] 2 5/8" |

| Mark the Highest grade of Par.121 Stud that allows the following for a 2 x 4 - 92 5/8” long: |
| --- |
|  | DEFECT |  |  | STUD | ECONOMY |
| 24. | Heavy skip on the NARROW FACE | [ ] | [ ] |
| 25. | Decay 1/3 the cross section | [ ] | [ ] |
| 26. | Wane 1/2W on the face full length | [ ] | [ ] |
| 27. | 1/2 inch of CROOK | [ ] | [ ] |
| 28. | A 2 inch EDGE Knot | [ ] | [ ] |
| 29. | A Split, 12 inches long | [ ] | [ ] |
| Mark the HIGHEST grade of Par. 122 Light Framing that allows the following for a 2 x 4 - 12 feet long: |
|  | DEFECT | CONSTRUCTION | STANDARD | UTILITY | ECONOMY |
| 30. | Slope of grain 1 in 6 | [ ] | [ ] | [ ] | [ ] |
| 31. | Skip 1/4 inch deep 4 feet long | [ ] | [ ] | [ ] | [ ] |
| 32. | White Speck 1/3 volume | [ ] | [ ] | [ ] | [ ] |
| 33. | Through Shake, 24 inches long | [ ] | [ ] | [ ] | [ ] |
| 34. | Wane 7/8 the Thickness on the END of the NARROW FACE | [ ] | [ ] | [ ] | [ ] |
| 35. | 100% White Speck | [ ] | [ ] | [ ] | [ ] |
| 36. | Split 1/3 length | [ ] | [ ] | [ ] | [ ] |
| 37. | 100% blue stain | [ ] | [ ] | [ ] | [ ] |
| 38. | Unsound wood 1/12W X 2”L | [ ] | [ ] | [ ] | [ ] |
| Mark the HIGHEST grade of Par. 124 Structural Light Framing and Joist & Planks that allows the following in a 2 x 6 - 20 feet long: |
|  | DEFECT | SEL STR | #1 | #2 | #3 | NONE |
| 39. | 50% Spike Knot | [ ] | [ ] | [ ] | [ ] | [ ] |
| 40. | Decay 1/3 the cross section | [ ] | [ ] | [ ] | [ ] | [ ] |
| 41. | Wane 1/2 thickness on the END | [ ] | [ ] | [ ] | [ ] | [ ] |
| 42. | Slope of Grain 1 in 8 | [ ] | [ ] | [ ] | [ ] | [ ] |
| 43. | 100 % Heart Stain | [ ] | [ ] | [ ] | [ ] | [ ] |
| 44. | Heavy Warp | [ ] | [ ] | [ ] | [ ] | [ ] |
| 45. | Skip 1/8 inch deep full length | [ ] | [ ] | [ ] | [ ] | [ ] |
| 46. | Through Shake 4 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 47. | Wane 1/2W X 3/4T full length | [ ] | [ ] | [ ] | [ ] | [ ] |
| 48. | Light Warp | [ ] | [ ] | [ ] | [ ] | [ ] |
| 49. | Wane 1/4 the Width Full Length | [ ] | [ ] | [ ] | [ ] | [ ] |
| 50. | 1 ½” Knot hole | [ ] | [ ] | [ ] | [ ] | [ ] |
| 51. | Split 9 inches long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 52. | Wane completely across Wide Face 2 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 53. | Through Shake 2 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 54. | 100% Blue Stain | [ ] | [ ] | [ ] | [ ] | [ ] |
| 55. | Wane 1/2 the Width X 4’ Long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 56. | Surface Shake full length | [ ] | [ ] | [ ] | [ ] | [ ] |

List the knot sizes for the following KD-HT 2 x 6’s

3 3/8"

57.	List the knot size:

SIZE

2 3/4"

58.	List the knot size:

1"

2"                  3/4"

# SIZE

59.	List the knot size

1/2"                                                                                                      5/8”

1 3/4”                                 1 3/4"                  SIZE

60.	List the knot size

1/2"

1/2"

3/4”

SIZE

# Text boxes

3 1/8"

1-3/4”