|  | ALBERTA FOREST PRODUCTS ASSOCIATION 500, 10709 Jasper Avenue EDMONTON, ALBERTA T5J 3N3 PHONE: (780) 452-2841 FAX: (780) 455-0505 |
| --- | --- |

A.F.P.A. SPRING 2008 GRADE EXAM

Name:		____________________________________	Date:	______________________

Company:	____________________________________	Location: ____________________

Mark the answer you choose with an [X]. ONLY ONE ANSWER PER QUESTION PLEASE!

| 1. | Which is NOT part of the trunk? |
| --- | --- |
|  | [ ] Pith | [ ] Sapwood | [ ] Leader | [ ] Cambium |

| 2. | Which part of the tree is NOT an ingredient of tree food? |
| --- | --- |
|  | [ ] Heart Wood | [ ] Moisture | [ ] Sap | [ ] Mineral Salts |

| 3. | The “Seat of Tree Growth” of the tree is called: |
| --- | --- |
|  | [ ] Pitch | [ ] Sap | [ ] Pits | [ ] Cambium |

| 4. | Inner bark is also called? |
| --- | --- |
|  | [ ] Cambium | [ ] Bast | [ ] Pits | [ ] Leader |

| 5. | Which is a desirable feature of lumber? |
| --- | --- |
|  | [ ] Re-grows Well | [ ] Susceptible to Decay | [ ] It Splits | [ ] It Burns |

| 6. | Which specie is being attacked by the “Mountain Pine Beetle”? |
| --- | --- |
|  | [ ] Engelmann Spruce | [ ] Douglas Fir | [ ] Lodgepole Pine | [ ] Tamarack |

| Mark the following DEFECTS under the correct CLASSIFICATION: |
| --- |
|  | Defect | Natural | Manufacturing | Seasoning |
| 7. | Grub Holes | [ ] | [ ] | [ ] |
| 8. | Shake | [ ] | [ ] | [ ] |
| 9. | Skip | [ ] | [ ] | [ ] |
| 10. | Twist | [ ] | [ ] | [ ] |
| 11. | Saw Cuts | [ ] | [ ] | [ ] |

| Mark the correct dressed WIDTH for the following: |
| --- |
| 12. | 2x4 S-GRN | [ ] 3 1/4" | [ ] 3 1/2" | [ ] 3 9/16" | [ ] 3 5/8" |
| 13. | 1x3 KD-HT | [ ] 2 1/4" | [ ] 2 1/2" | [ ] 2 9/16” | [ ] 3” |
| 14. | 2x6 S-GRN | [ ] 5 3/8" | [ ] 5 1/2" | [ ] 5 1/4 " | [ ] 5 5/8" |
| 15. | 2x8 S-DRY | [ ] 7 1/4" | [ ] 7 1/2" | [ ] 7 9/16" | [ ] 7 5/8" |
| 16. | 2x10 S-DRY | [ ] 9 1/4" | [ ] 9 1/2" | [ ] 9 9/16" | [ ] 9 5/8" |

| Mark the correct dressed THICKNESS for the following: |
| --- |
| 17. | 1x6 S-GRN | [ ] 3/4" | [ ] 7/8" | [ ] 25/32" | [ ] 1" |
| 18. | 2x4 KD-HT | [ ] 1 7/16" | [ ] 1 1/2" | [ ] 1 9/16" | [ ] 1 5/8" |
| 19. | 3x6 S-GRN | [ ] 2 7/16" | [ ] 2 1/2" | [ ] 2 9/16" | [ ] 2 5/8" |
| 20. | 4x8 S-GRN | [ ] 3 7/16" | [ ] 3 1/2" | [ ] 3 9/16" | [ ] 3 5/8" |

21- 24.		Match the characteristics with the description: (e.g.     a    )

a)	Over 1/8” deep

21.	Hit or Miss Skip	_________

b)	Not Over 1/16” Deep

c)	Not Over 1/8” Deep				22.	1/3 Length of a 7’	__________

d)	28” long

23.	1/6 the length of a 10’ __________

e)	20” long

f)	32” long					24.	Very Heavy Skip	__________

| Mark the Highest grade of Par.121 Stud that allows the following for a 2 x 6 - 92 5/8” long: |
| --- |
|  | DEFECT |  |  | STUD | ECONOMY |
| 25. | 1/8 inch skip 2’ in length on the EDGE | [ ] | [ ] |
| 26. | 50% White Speck | [ ] | [ ] |
| 27. | Warp ½ Medium | [ ] | [ ] |
| 28. | Wane ¾ the wide face full length | [ ] | [ ] |
| 29. | Wane ¾ the edge on the end 4” long | [ ] | [ ] |
| 30. | Through shake 1/3 the length | [ ] | [ ] |

| Mark the HIGHEST grade of Par. 122 Light Framing that allows the following for a 2 x 4 – 8 feet long: |
| --- |
|  | DEFECT | CONSTRUCTION | STANDARD | UTILITY | ECONOMY |
| 31. | Through Shake 2’ Long | [ ] | [ ] | [ ] | [ ] |
| 32. | Skip 1/16 inch deep full length | [ ] | [ ] | [ ] | [ ] |
| 33. | Rot 1/12 Width X 2” Long | [ ] | [ ] | [ ] | [ ] |
| 34. | Split 4” long | [ ] | [ ] | [ ] | [ ] |
| 35. | Wane ½ Width X ½ Thickness full length. | [ ] | [ ] | [ ] | [ ] |
| 36. | ¼” Skip for 2’ long | [ ] | [ ] | [ ] | [ ] |
| 37. | Wane 1/2 the wide face FULL LENGTH | [ ] | [ ] | [ ] | [ ] |
| 38. | 2 5/8” Round knot | [ ] | [ ] | [ ] | [ ] |
| 39. | 2” Round Knot | [ ] | [ ] | [ ] | [ ] |
| 40. | Warp ½ medium | [ ] | [ ] | [ ] | [ ] |

| Mark the HIGHEST grade of Par. 124 Structural Joist & Planks that allows the following in a 2 x 6 – 16 feet long: |
| --- |
|  | DEFECT | Sel. STR. | #2 STR. | #3 STR. | NONE |
| 41. | Wane 1/4 the thickness FULL LENGTH | [ } | [ ] | [ ] | [ ] |
| 42. | Rot 1/3 the width 2” long | [ ] | [ ] | [ ] | [ ] |
| 43. | 50% White Speck | [ ] | [ ] | [ ] | [ ] |
| 44. | Split 16” long | [ ] | [ ] | [ ] | [ ] |
| 45. | Wane 2/3 the thickness on the END X 6” long | [ ] | [ ] | [ ] | [ ] |
| 46. | Slope of Grain 1 in 3 | [ ] | [ ] | [ ] | [ ] |
| 47. | 10% Heart Stain | [ ] | [ ] | [ ] | [ ] |
| 48. | Surface Shake 3’ Long | [ ] | [ ] | [ ] | [ ] |
| 49. | Wane 2/3 W X 2/3 T FULL LENGTH | [ ] | [ ] | [ ] | [ ] |
| 50. | Through Shake 4’ Long | [ ] | [ ] | [ ] | [ ] |
| 51. | Skip 1/64 inch deep full length | [ ] | [ ] | [ ] | [ ] |

| Mark the HIGHEST grade of Par. 113 Boards that allows the following on the FACE of a 1 x 8 - 12 feet long: |
| --- |
|  | DEFECT | #2 Common | #3 Common | #4 Common | #5 Common |
| 52. | White Speck 1/8 face | [ ] | [ ] | [ ] | [ ] |
| 53. | Skip | [ ] | [ ] | [ ] | [ ] |
| 54. | 4” Knot Hole | [ ] | [ ] | [ ] | [ ] |
| 55. | Torn Grain | [ ] | [ ] | [ ] | [ ] |
| 56. | Split 1/4 the length | [ ] | [ ] | [ ] | [ ] |

List the knot sizes for the following KD-HT 2 x 6’s

2 1/2"

57.	List the knot size:

SIZE

2 3/4"

58.	List the knot size:

1"

1 3/8 "          15/16"

# SIZE

59.	List the knot size

1"

3/8"

2 3/4”                                                          SIZE

60.	List the knot size

1/4”

1/2"

1”

SIZE

# Text boxes

3 3/4"

1-3/4”