|  |  | ALBERTA FOREST PRODUCTS ASSOCIATION 500, 10709 Jasper Avenue EDMONTON, ALBERTA T5J 3N3 PHONE: (780) 452-2841 FAX: (780) 455-0505 |
| --- | --- | --- |

A.F.P.A. SPRING 2012 GRADE EXAM

Name:		____________________________________	Date:	______________________

Company:	____________________________________	Location: ____________________

Mark the answer you choose with an [X]. ONLY ONE ANSWER PER QUESTION PLEASE!

| 1. | Which of the following species is NOT in the SPF group? |
| --- | --- |
|  | [ ] White Spruce | [ ] Red Spruce | [ ] Black Spruce | [ ] Sitka Spruce |

| 2. | A portion of a branch or limb cut through by a saw, gives us what kind of defect? |
| --- | --- |
|  | [ ] Splits | [ ] Knots | [ ] Shake | [ ] Skip |

| 3. | An indication that a piece of lumber contains SLOPE of GRAIN is? |
| --- | --- |
|  | [ ] Twist | [ ] Cup | [ ] Skip | [ ] Shake |

| 4. | A series of SKIPS 1/16 inch deep with surfaced areas in between, skipped areas NOT over 4 feet long. Would be classified as? |
| --- | --- |
|  | [ ] Hit or Miss | [ ] Heavy Skip | [ ] Hit and Miss | [ ] Full Sawn |

| 5. | What piece of information, is NOT required to be on a Grade Stamp: |
| --- | --- |
|  | [ ] Mill ID Number | [ ] Species Group | [ ] Length of piece | [ ] NLGA |

6-9.		Match the following Abbreviations with their correct meaning. (e.g.     a    )

a)	S-GRN

6.	Surface Dry			_________

b)	STK

c)	S-DRY						7.	Heat-treated			__________

d)	KD

8.	Kiln-dried			__________

e)	S&T

f)	HT						9.	Sound and Tight		__________

| Mark the following DEFECTS under the correct CLASSIFICATION: |
| --- |
|  | Defect | Natural | Manufacturing | Seasoning |
| 10. | Splits | [ ] | [ ] | [ ] |
| 11. | White Speck | [ ] | [ ] | [ ] |
| 12. | Torn Grain | [ ] | [ ] | [ ] |
| 13. | Rot | [ ] | [ ] | [ ] |

| Match the following MANUFACTURING DEFECTS to the correct DEPTH CLASSIFICATION: |
| --- |
|  | DEFECT | 1/64" | 1/32" | 1/16" | 1/8" | Over 1/8" |
| 14. | Very Heavy Skip | [ ] | [ ] | [ ] | [ ] | [ ] |
| 54. | Heavy Mismatch | [ ] | [ ] | [ ] | [ ] | [ ] |
| 16. | Medium Offset | [ ] | [ ] | [ ] | [ ] | [ ] |
| 17. | Light Machine Bite | [ ] | [ ] | [ ] | [ ] | [ ] |

| Mark the correct dressed WIDTH for the following: |
| --- |
| 18. | 2 x 10 S-GRN HT | [ ] 9 1/2" | [ ] 10" | [ ] 9 9/16" | [ ] 9 5/8" |
| 19. | 2 x 6 KD-HT | [ ] 5 1/2" | [ ] 5 5/8" | [ ] 6” | [ ] 5 9/16" |
| 20. | 2 x 8 KD-HT | [ ] 7 9/16" | [ ] 7 1/2" | [ ] 7 5/8 " | [ ] 7 1/4" |
| 21. | 2 x 4 S-DRY | [ ] 3 1/4" | [ ] 3 3/4" | [ ] 3 1/2" | [ ] 3 7/8" |

| Mark the correct dressed THICKNESS for the following: |
| --- |
| 22. | 2 x 4 S-GRN HT | [ ] 1 3/4" | [ ] 1 9/16" | [ ] 1 5/8"" | [ ] 1 1/2" |
| 23. | 2 x 6 KD-HT | [ ] 1 7/16" | [ ] 1 1/2" | [ ] 1 9/16" | [ ] 1 5/8" |
| 24. | 4 x 6 S-DRY | [ ] 3 1/2 | [ ] 3 9/16 | [ ] 4 | [ ] 3 1/4 |
| 25. | 1 x 10 KD-HT | [ ] 3/4" | [ ] 25/32" | [ ] 15/16" | [ ] 1" |

| Mark the Highest grade of Par.121 Stud that allows the following for a 2 x 4 - 92 5/8” long: |
| --- |
|  | DEFECT |  |  | STUD | ECONOMY |
| 26. | Skip 1/8" deep on NARROW FACE 2’ long | [ ] | [ ] |
| 27. | Decay 1/3 cross section | [ ] | [ ] |
| 28. | Wane 1/3 thickness full length | [ ] | [ ] |
| 29. | A 1 3/4 inch CENTERLINE knot | [ ] | [ ] |
| 30. | A 2 1/2 inch EDGE Knot | [ ] | [ ] |
| 31. | Wane 3/4 width on end 1 foot long | [ ] | [ ] |
| Mark the HIGHEST grade of Par. 122 Light Framing that allows the following for a 2 x 4 8 feet long: |
|  | DEFECT | CONSTRUCTION | STANDARD | UTILITY | ECONOMY |
| 32. | Wane 1/3 T X 1/3 W full length | [ ] | [ ] | [ ] | [ ] |
| 33. | Surface Shake 3 feet long | [ ] | [ ] | [ ] | [ ] |
| 34. | Full length Wane, 1/2 thickness | [ ] | [ ] | [ ] | [ ] |
| 35. | Decay 1/4 cross section | [ ] | [ ] | [ ] | [ ] |
| 36. | Split 4 inches long | [ ] | [ ] | [ ] | [ ] |
| 37. | Split 16 inches long | [ ] | [ ] | [ ] | [ ] |
| 38. | Wane completely through narrow face on end | [ ] | [ ] | [ ] | [ ] |
| 39. | Eight 1 3/4 inch Knot Holes | [ ] | [ ] | [ ] | [ ] |
| 40. | 2 1/2 inch Round Knot | [ ] | [ ] | [ ] | [ ] |
| Mark the HIGHEST grade of Par. 124 Structural Light Framing and Joist & Planks that allows the following in a 2 x 6-12 feet long: |
|  | DEFECT | SEL STR | #1 | #2 | #3 | NONE |
| 41. | White Speck 1/3 the volume | [ ] | [ ] | [ ] | [ ] | [ ] |
| 42. | Wane on END 2/3 width | [ ] | [ ] | [ ] | [ ] | [ ] |
| 43. | Wane 1/2 thickness on the END | [ ] | [ ] | [ ] | [ ] | [ ] |
| 44. | Slope of Grain 1 in 4 | [ ] | [ ] | [ ] | [ ] | [ ] |
| 45. | 80% Sap Stain | [ ] | [ ] | [ ] | [ ] | [ ] |
| 46. | A 2 3/4 inch EDGE Knot | [ ] | [ ] | [ ] | [ ] | [ ] |
| 47. | Skip 1/16 inch deep 4 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 48. | Through Shake 5 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 49. | Wane 1/2 T x 1/2 W full length | [ ] | [ ] | [ ] | [ ] | [ ] |
| 50. | Medium Warp | [ ] | [ ] | [ ] | [ ] | [ ] |
| 51. | Decay 3 inches long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 52. | A 2 inch Centerline Knot | [ ] | [ ] | [ ] | [ ] | [ ] |
| 53. | Split 8 inches long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 54. | Wane completely across Wide Face 1 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 55. | Surface Shake 4’L | [ ] | [ ] | [ ] | [ ] | [ ] |
| 56. | 12 Grub Holes | [ ] | [ ] | [ ] | [ ] | [ ] |

List the knot sizes for the following KD-HT 2 x 4’s

1	1/2"

57.	List the knot size:

SIZE

1 3/4 "

58.	List the knot size:

1/2"

SIZE

2"                  3/4"

59.	List the knot size

3/4"									  3/4"

SIZE

1 3/4”                                 1 3/4"

60.	List the knot size

1/2”                                                                                                     1/2"

3/4”	SIZE

# Text boxes

1 7/8"

1-3/4”