|  |  | ALBERTA FOREST PRODUCTS ASSOCIATION 900, 10707 100th Avenue EDMONTON, ALBERTA T5J 3M1 PHONE: (780) 452-2841 FAX: (780) 455-0505 |
| --- | --- | --- |

A.F.P.A. FALL 2013 & SPRING 2014 GRADE EXAM

Name:		____________________________________	Date:	______________________

Company:	____________________________________	Location: ____________________

Mark the answer you choose with an [X]. ONLY ONE ANSWER PER QUESTION PLEASE!

| 1. | The newest growth in height is called: |
| --- | --- |
|  | [ ] Trunk | [ ] Leader | [ ] Cambium | [ ] Bast |

| 2. | The inner bark is also called: |
| --- | --- |
|  | [ ] Sapwood | [ ] Seat of Tree Growth | [ ] Bast | [ ] Cambium |

| 3. | The healing agent in the tree is called: |
| --- | --- |
|  | [ ] Bark | [ ] Cambium | [ ] Pith | [ ] Pitch |

| 4. | Water contained in the cell walls is called: |
| --- | --- |
|  | [ ] Free Water | [ ] Bound Water | [ ] Hard Water | [ ] Soft Water |

| 5. | Which specie is being attacked by the “Mountain Pine Beetle”? |
| --- | --- |
|  | [ ] Douglas Fir | [ ] Balsam Fir | [ ] Lodgepole Pine | [ ] Tamarack |

| 6. | Which of the following specie is in the S-P-F species group: |
| --- | --- |
|  | [ ] Tamarack | [ ] Douglas Fir | [ ] Jack Pine | [ ]Sitka Spruce |

| 7. | Lumber grade stamped KD-HT or S-DRY must not exceed what Moisture Content? |
| --- | --- |
|  | [ ] 10% | [ ] 15% | [ ] 19% | [ ] 26% |

| 8. | Fibre saturation point occurs at approximately: |  |
| --- | --- | --- |
|  | [ ] 10% | [ ] 15% | [ ] 19% | [ ] 26% |  |

| 9. | A piece of lumber that dries from 85% MC to 45% MC will become: |
| --- | --- |
|  | [ ] Stronger | [ ] Lighter | [ ] Brighter | [ ] Durable |

10-13.		Match the characteristics with the description. (e.g.     a    )

a)	14” long

10.	1/4 the length of a 7’		_________

b)	60” long

c)	32” long					11.	1/3 the length of a 8’		__________

d)	22” long

12.	1/6 the length of a 12’		__________

e)	21” long

f)	24” long					13.	1/2 the length of a 10’		__________

| Match the following MANUFACTURING DEFECTS to the correct DEPTH CLASSIFICATION: |
| --- |
|  | DEFECT | 1/64" | 1/32" | 1/16" | 1/8" | Over 1/8" |
| 14. | Light Machine Gouge | [ ] | [ ] | [ ] | [ ] | [ ] |
| 54. | Medium Torn Grain | [ ] | [ ] | [ ] | [ ] | [ ] |
| 16. | Very Heavy Offset | [ ] | [ ] | [ ] | [ ] | [ ] |
| 17. | Heavy Skip | [ ] | [ ] | [ ] | [ ] | [ ] |
| Mark the correct dressed WIDTH for the following: |
| 18. | 2 x 10 S-GRN | [ ] 9 1/4" | [ ] 9 3/4" | [ ] 9 1/2" | [ ] 10" |
| 19. | 2 x 6 S-GRN HT | [ ] 5 1/2" | [ ] 5 5/8" | [ ] 6” | [ ] 5 9/16" |
| 20. | 2 x 4 KD-HT | [ ] 3 9/16" | [ ] 3 1/2" | [ ] 3 5/8" | [ ] 3 1/4" |
| 21. | 2 x 3 S-DRY | [ ] 2 1/4" | [ ] 2 3/4" | [ ] 2 1/2" | [ ] 3" |

| Mark the correct dressed THICKNESS for the following: |
| --- |
| 22. | 2 x 10 S-DRY | [ ] 1 3/4" | [ ] 1 9/16" | [ ] 1 5/8"" | [ ] 1 1/2" |
| 23. | 4 x 10 KD-HT | [ ] 3 7/16" | [ ] 3 1/2" | [ ] 3 9/16" | [ ] 3 5/8" |
| 24. | 3 x 10 S-GRN | [ ] 2 1/2 | [ ] 2 9/16 | [ ] 3 | [ ] 2 1/4 |
| 25. | 1 x 10 KD-HT | [ ] 3/4" | [ ] 25/32" | [ ] 15/16" | [ ] 1" |

| Mark the Highest grade of Par.121 Stud that allows the following for a 2 x 4 - 92 5/8” long: |
| --- |
|  | DEFECT |  |  | STUD | ECONOMY |
| 26. | Skip 1/8” for 2’ long on the edge | [ ] | [ ] |
| 27. | 100% firm White Speck | [ ] | [ ] |
| 28. | Wane 1/3 thickness full length | [ ] | [ ] |
| 29. | Skip 1/16” full length on one wide face | [ ] | [ ] |
| 30. | Edge Knot 50% displacement | [ ] | [ ] |
| 31. | Split twice the width of the piece | [ ] | [ ] |
| Mark the HIGHEST grade of Par. 122 Light Framing that allows the following for a 2 x 4 - 16 feet long: |
|  | DEFECT | CONSTRUCTION | STANDARD | UTILITY | ECONOMY |
| 32. | Wane 1/2 T X 3/4 W full length | [ ] | [ ] | [ ] | [ ] |
| 33. | Surface Shake 2 feet long | [ ] | [ ] | [ ] | [ ] |
| 34. | Wane 1/3 thickness full length | [ ] | [ ] | [ ] | [ ] |
| 35. | Decay 1/2 the cross section | [ ] | [ ] | [ ] | [ ] |
| 36. | White Speck 50% of the volume | [ ] | [ ] | [ ] | [ ] |
|  | DEFECT | CONSTRUCTION | STANDARD | UTILITY | ECONOMY |
| 37. | Split 9 inches long | [ ] | [ ] | [ ] | [ ] |
| 38. | Wane completely through narrow face on the end | [ ] | [ ] | [ ] | [ ] |
| 39. | Medium warp | [ ] | [ ] | [ ] | [ ] |
| 40. | Firm White Speck | [ ] | [ ] | [ ] | [ ] |
| Mark the HIGHEST grade of Par. 124 Structural Light Framing and Joist & Planks that allows the following in a 2 x 4-16 feet long: |
|  | DEFECT | SEL STR | #1 | #2 | #3 | NONE |
| 41. | White Speck 1/3 the volume | [ ] | [ ] | [ ] | [ ] | [ ] |
| 42. | Wane on END 3/4 width | [ ] | [ ] | [ ] | [ ] | [ ] |
| 43. | Wane 2/3 thickness on the END | [ ] | [ ] | [ ] | [ ] | [ ] |
| 44. | Slope of Grain 1 in 12 | [ ] | [ ] | [ ] | [ ] | [ ] |
| 45. | 10% Heart Stain | [ ] | [ ] | [ ] | [ ] | [ ] |
| 46. | Decay on the face 1/6W x 2”long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 47. | Skip 1/8 inch deep 3 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 48. | Three Face Shake 5 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 49. | Wane 1/4 T x 1/4 W full length | [ ] | [ ] | [ ] | [ ] | [ ] |
| 50. | Light Warp | [ ] | [ ] | [ ] | [ ] | [ ] |
| 51. | 100% heart stain | [ ] | [ ] | [ ] | [ ] | [ ] |
| 52. | Through shake 2 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 53. | Split 1/6 the length | [ ] | [ ] | [ ] | [ ] | [ ] |
| 54. | Wane completely across Wide Face 1 feet long on the end | [ ] | [ ] | [ ] | [ ] | [ ] |
| 55. | Surface Shake 5 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 56. | 1240 Grub Holes on one face | [ ] | [ ] | [ ] | [ ] | [ ] |

List the knot sizes for the following KD-HT 2 x 4’s

1 3/8"

57.	List the knot size:

SIZE

2 7/8 "

58.	List the knot size:

3/4"

SIZE

2"                  1 1/4"

59.	List the knot size

3/8"									  3/8"

SIZE

1 3/4”                                 1 3/4"

60.	List the knot size

1/2”                                                                                                     1/2"

3/4”	SIZE

# Text boxes

2 3/8"

1-3/4”