|  |  | ALBERTA FOREST PRODUCTS ASSOCIATION 900, 10707 100th Avenue EDMONTON, ALBERTA T5J 3M1 PHONE: (780) 452-2841 FAX: (780) 455-0505 |
| --- | --- | --- |

A.F.P.A. FALL 2014 & SPRING 2015 GRADE EXAM

Name:		____________________________________	Date:	______________________

Company:	____________________________________	Location: ____________________

Mark the answer you choose with an [X]. ONLY ONE ANSWER PER QUESTION PLEASE!

| 1. | The portion of a branch or limb cut through by a saw, results in what type of defect? |
| --- | --- |
|  | [ ] Warp | [ ] Knot | [ ] Checks | [ ] Shake |

| 2. | Which is NOT part of the trunk: |
| --- | --- |
|  | [ ] Pith | [ ] Sapwood | [ ] Bark | [ ] Leaves |

| 3. | What part of the tree manufactures tree food: |
| --- | --- |
|  | [ ] Crown | [ ] Heartwood | [ ] Sapwood | [ ] Bast |

| 4. | A coniferous tree have: |
| --- | --- |
|  | [ ] Nuts | [ ] Leaves | [ ] Needles | [ ] None of these |

| 5. | What piece of information, IS required to be on a Grade Stamp: |
| --- | --- |
|  | [ ] NLGA | [ ] CLSAB | [ ] Date | [ ] Grader ID |

6-9.		Match the following Abbreviations with their correct meaning. (e.g.     a    )

a)	KND

6.	Surface Dry			_________

b)	STK

c)	S-DRY						7.	Heat-treated			__________

d)	KD

8.	Kiln-dried			__________

e)	S&T

f)	HT						9.	Sound and Tight		__________

| Mark the following DEFECTS under the correct CLASSIFICATION: |
| --- |
|  | Defect | Natural | Manufacturing | Seasoning |
| 10. | Three face Knots | [ ] | [ ] | [ ] |
| 11. | Through shake | [ ] | [ ] | [ ] |
| 12. | Through Checks | [ ] | [ ] | [ ] |
| 13. | Very Light Skip | [ ] | [ ] | [ ] |

| Match the following MANUFACTURING DEFECTS to the correct DEPTH CLASSIFICATION: |
| --- |
|  | DEFECT | 1/64" | 1/32" | 1/16" | 1/8" | Over 1/8" |
| 14. | Medium Skip | [ ] | [ ] | [ ] | [ ] | [ ] |
| 54. | Heavy Loosened Grain | [ ] | [ ] | [ ] | [ ] | [ ] |
| 16. | Very Light Offset | [ ] | [ ] | [ ] | [ ] | [ ] |
| 17. | Light Mismatch | [ ] | [ ] | [ ] | [ ] | [ ] |
| Mark the correct dressed THICKNESS for the following: |
| 18. | 2 x 4 S-GRN | [ ] 1 1/2" | [ ] 3/4" | [ ] 1 9/16" | [ ] 1 5/8" |
| 19. | 1 x 6 S-GRN HT | [ ] 1/2" | [ ] 5/8" | [ ] 3/4” | [ ] 25/32" |
| 20. | 3x 8 KD-HT | [ ] 2 9/16" | [ ] 2 1/2" | [ ] 2 5/8 " | [ ] 2 1/4" |
| 21. | 4 x 10 S-DRY | [ ] 3 1/4" | [ ] 3 3/4" | [ ] 3 1/2" | [ ] 4" |

| Mark the correct dressed WIDTH for the following: |
| --- |
| 22. | 2 x 10 S-GRN HT | [ ] 9 3/4" | [ ] 9 9/16" | [ ] 9 5/8"" | [ ] 9 1/2" |
| 23. | 2 x 8 KD-HT | [ ] 7 1/4" | [ ] 7 1/2" | [ ] 7 9/16" | [ ] 7 5/8" |
| 24. | 3 x 6 S-GRN | [ ] 5 1/2 | [ ] 5 9/16 | [ ] 5 5/8” | [ ] 6 |
| 25. | 1 x 4 S-GRN | [ ] None of these | [ ] 3 3/4" | [ ] 1 7/16" | [ ] 4" |

| Mark the Highest grade of Par.121 Stud that allows the following for a 2 x 4 - 104 5/8” long: |
| --- |
|  | DEFECT |  |  | STUD | ECONOMY |
| 26. | Wane 1/2 thickness on the end | [ ] | [ ] |
| 27. | Wane 1/2 width on the end | [ ] | [ ] |
| 28. | 100% soft Honeycomb | [ ] | [ ] |
| 29. | Skip 1/8” on one edge 2’ Long | [ ] | [ ] |
| 30. | Spike Knot 55% displacement | [ ] | [ ] |
| 31. | Split Twice the Width | [ ] | [ ] |
| Mark the HIGHEST grade of Par. 122 Light Framing that allows the following for a 2 x 4 - 16 feet long: |
|  | DEFECT | CONSTRUCTION | STANDARD | UTILITY | ECONOMY |
| 32. | White Speck 50% of the volume | [ ] | [ ] | [ ] | [ ] |
| 33. | White Speck 100% of volume | [ ] | [ ] | [ ] | [ ] |
| 34. | Full length wane, 1/3 thickness | [ ] | [ ] | [ ] | [ ] |
| 35. | Decay 1/2 the cross section | [ ] | [ ] | [ ] | [ ] |
| 36. | Knot 1 ½” on the edge of face | [ ] | [ ] | [ ] | [ ] |
| 37. | Split 1 ½ X Width | [ ] | [ ] | [ ] | [ ] |
| 38. | Wane completely across the wide face on the end | [ ] | [ ] | [ ] | [ ] |
| 39. | ½ Medium warp | [ ] | [ ] | [ ] | [ ] |
| 40. | Through shake 24” Long | [ ] | [ ] | [ ] | [ ] |
| Mark the HIGHEST grade of Par. 124 Structural Light Framing and Joist & Planks that allows the following in a 2 x 4-20 feet long: |
|  | DEFECT | SEL STR | #1 | #2 | #3 | NONE |
| 41. | White Speck 1/4 the volume | [ ] | [ ] | [ ] | [ ] | [ ] |
| 42. | White Speck 1/3 the volume | [ ] | [ ] | [ ] | [ ] | [ ] |
| 43. | Wane 1/2 thickness on the END | [ ] | [ ] | [ ] | [ ] | [ ] |
| 44. | Slope of Grain 1 in 6 | [ ] | [ ] | [ ] | [ ] | [ ] |
| 45. | Heart Stain | [ ] | [ ] | [ ] | [ ] | [ ] |
| 46. | Sap Stain | [ ] | [ ] | [ ] | [ ] | [ ] |
| 47. | Skip 1/8 inch deep full length | [ ] | [ ] | [ ] | [ ] | [ ] |
| 48. | Through Shake 2 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 49. | Wane 1/2 T x 1/2 W full length | [ ] | [ ] | [ ] | [ ] | [ ] |
| 50. | Wane ½ T x ½ W Maximum Equiv. | [ ] | [ ] | [ ] | [ ] | [ ] |
| 51. | Decay 4 inches long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 52. | Through Check 2 feet long | [ ] | [ ] | [ ] | [ ] | [ ] |
| 53. | Split 1 ½ X Width of the piece | [ ] | [ ] | [ ] | [ ] | [ ] |
| 54. | Surface shake full length | [ ] | [ ] | [ ] | [ ] | [ ] |
| 55. | Surface Shake 10’L | [ ] | [ ] | [ ] | [ ] | [ ] |
| 56. | Warp unrestricted (+) | [ ] | [ ] | [ ] | [ ] | [ ] |

List the knot sizes for the following KD-HT 2 x 4’s

1 1/4"

57.	List the knot size:

SIZE

1 3/4 "

58.	List the knot size:

3/4"

SIZE

1 1/8"                  1 1/4"

59.	List the knot size

1"									  3/4"

SIZE

1 3/4”                                 1 3/4"

60.	List the knot size

1”                                                                                                       1/2"

3/4”	SIZE

# Text boxes

1 3/8"

1-3/4”